## Slide 1: Low-Cost, Portable, Pneumonia Diagnostic Device
Sheun Aluko
Team Members: Lauren Bedell and Clark Ingram
Mentor: Dr. Dan Moran

## Slide 2: Global Prevalence of Pneumonia
References:
World Health Organization. "Pneumonia." ; World Health Organization “The top 10 causes of death”; http://www.who.int/mediacentre/factsheets/fs310/en/index4.html
Notes: WHO places LRTI’s as the 4th leading cause of death in the world in 2012, accounting for approximately 5.5% of annual global mortality
However in low-income level countries the world health organization reports that lower respiratory tract infections are the leading cause of death indicating there is still a significant need for improved methods of pneumonia diagnosis and treatment in developing countries

## Slide 3: Need and Project Scope
Low-Cost, Portable, Adult Pneumonia Diagnostic Device with high usability in Developing Countries
High cost of pre-existing devices
Limited number of technicians
Limited number of physicians
Unreliable electricity
High prevalence of pneumonia
Notes: A multitude of individuals needing prompt diagnosis and treatment
Limited number of technicians to operate available equipment
Limited number of trained medical staff to interpret images and chest sounds
Limited access to electricity for diagnostic equipment

## Slide 4: Overview of Device Modules

## Slide 5: Signal Acquisition Module
Three main components
  Diaphragm to pick up vibrations
  Chamber to direct acoustic vibrations to microphone
  Microphone for signal transduction
Adafruit Electret Microphone Amplifier-MAX4466 with Adjustable Gain
Littman: 36556 Tunable Diaphragm and Rim Assembly

## Slide 6: Signal Processing Module
Analog to digital convertor for input signal
Microprocessor for pneumonia classification
Specification | Value
Length of Audio Sample | 15 seconds
Sampling Rate (Samples/s) | 8,000 Hz
Sample Bit Resolution (Bits/s) | 10 bits
Memory Type | Size | Quantity
Buffer (for calculations) | 146.5 KB | 2
Buffer (for stored values) | 1 byte | 5
Data Storage (for processed signal) | 146.5 KB | 1
TOTAL MEMORY NEEDED | 439.505 KB | NA
ADC Bit Size | 10
ADC Sampling Speed | 8,000 Hz
Microcontroller Memory | > 440 KB
Microcontroller Analog Inputs | 1
Microcontroller Digital Inputs | 1
Microcontroller Digital Outputs | 8

## Slide 7: Software Process
Notes: LF wheezes, coarse crackles
HF wheezes, fine crackles
High frequency noise due to airflow turbulence

## Slide 8: User Interface Module
Two main components
  Switch to initiate recording
  Display for pneumonia classification results
Adafruit Tactile Button Switch
LUMEX 0.5in 2-Digit 7-Segment Display

## Slide 9: Power Module
Two main components
  Battery to power device electronics
  Regulated voltage supply
Part | Current | Power
MSP430 (micro-controller) | 0.6 mA | 1.8mW
microphone | 0.5 mA | 1.5mW
amplifier | 24 uA | 0.072mW
Dual LED | ~ | 105 mW
LED driver (2) | ~ | 1000 mW
Total | ~ | 1.108 W
Sparkfun Polymer Lithium Ion Battery
Sparkfun Low Drop Fixed and Adjustable Positive Voltage Regulator

## Slide 10: Device Connectivity

## Slide 11: Parts, Manufacturing, and Assembly
<$150 and <0.5 kg
Notes: Obtaining -> majority can be shipped with standard ground sipping with minimal lead times
Assembly -> Use of industrial adhesives and soldering
Take away ? <$150 and <0.5 kg

## Slide 12: Proof of Concept / Prototype

## Slide 13: Conclusions
Was the problem resolved?
  LDA classifier training
  Regulatory approval
Future Directions?
  Clinical trial
  Improved device components and assembly
    ADC, microphone, DSP
IP
  Device components licensed
  Software algorithm and application of licensed devices may be patentable
  Completely functional prototype yet to be made
What did we learn?
  Foresight and planning crucial
  Co-dependency of device components
  Engineering design is not an individual process
    Diversity of skillsets
    Division of work
    Time management

## Slide 14: Acknowledgements
Team Members:
  Lauren Bedell
  Clark Ingram
Mentor: Dr. Dan Moran
Professor: Dr. Joseph Klaesner
TA: Rebecca Gilson

## Slide 15: Questions?

## Slide 16: PCB Schematic

## Slide 17: Assembled Device Enclosure

## Slide 18: Frequency Band Information

## Slide 19: Pneumonia Detection

## Slide 20: LDA Visualization

## Slide 21: Parts